Contents

I. Solar Energy In Turkey 									2

A. State of the Market 									2

B. Solar Energy Potential of Turkey 							3

C. Domestic Production of Solar Panels 							6

D. Domestic Market of Solar Panels 							8

E. Foreign Trade 									8

F. Research & Development in the Sector 						10

G. Governmental Institutions Operating in the Sector 					20

II. LegIslatIon & Government PolIcIes In Solar Energy Sector In Turkey		21

I. Solar Energy In Turkey

A. State of the Market

The leading solar technology in Turkey is that of the ﬂat-plate solar collectors. Flat-plate solar collectors were ﬁrst employed at the beginning of 1970’s in tourist hotels and summer houses located in western coastal areas of Turkey. Simple technology, brought from neighbouring Mediterranean countries in Europe (Italy, Greece), was copied and adopted to the local economical capacities of small workshop manufacturers. The urgent need to supply hot water in touristic towns and coastal vacation houses in summer months mushroomed the production of the ﬂat-plate solar collectors and the number of manufacturers. Production was rapidly expanded from the Aegean (Izmir, Kusadası, Ayvalık) region to the south-west (Marmaris, Fethiye, Mugla) and southern coastal areas (Antalya, Alanya, Mersin, Adana, Hatay) and, in the last decade, to south-eastern towns (Diyarbakir, Gaziantep, Urfa). This inexpensive method of hot water production from the sun for domestic use was welcomed by the public in seventies and eighties. This led to an increase in the number of collector production companies and growing collector sales.

Resistant tempered glass is used in glazed thermal solar collectors for covering the surface area. Tempered glass is produced in major by the largest Turkish glass ﬁrm of TSCF-Turkiye Sise Cam Fabrikaları A.S. (www.sisecam.com.tr).

Compared with the developed countries of USA, Japan, and the Sun Belt countries, Turkey is a major user of solar technology, especially for solar thermal systems. The solar collector market now is based on two different types of solar collectors: technologically poor traditional collectors and technologically advanced high efﬁciency ones. Technologically poor collectors are marked by low efﬁciency and bad quality, while high efﬁciency types consist of selective surfaces raising overall system performance and, with it, the price.

Nowadays, some attempts have been made to use the sun as a natural heat source by building solar houses. In Turkey, solar buildings are beginning to ﬁnd a place in new building designs and developments.

Turkey is located in the Sunbelt and is therefore rich in solar energy. Using solar energy for various purposes already attracts consumers. People are using solar energy mostly in domestic hot water systems, as well as electricity production. Solar collector producers take full advantage of this situation in inﬂuencing consumers. In many congresses and/or fairs, producers attend to advertise their products. Also, TV ads and advertising papers attract consumer attention to solar thermal systems. Consumers use such technology and take full advantage of their installed systems, especially in their summer resorts, for the rapid availability of hot water for their daily needs, for free heating of water and for low-cost of maintenance of production systems. Industrial users, such as hotels and industrial facilities, improve their image through the employment of clean energy based systems and of course lower energy-related expenses.

B. Solar Energy Potential of Turkey

Currently, there isn’t any licensed producer of solar energy in Turkey. However, Turkey is located in a relatively advantageous geographical position for solar energy production. According to Ministry of Energy and Natural Resources, the potential of electricity production using solar energy in Turkey is 380 billion kWh/year, which is approximately two times of the total electricity production of the country. The solar energy potential evaluations made by EIE (General Directorate of Electrical Power Resources Survey and Development Administration), based on the data measured by DMI (State Meteorological Services) during 1966-1982 revealed:

- The annual average total insolation duration as 2640 hours (7.2 hours/day)

- Average annual solar radiation as 1311 kWh/m²-year (3.6 kWh/m²-day)

- Total solar energy potential of Turkey is calculated as 35 Mtoe per year.

- Solar energy production is expected  to reach 602 Ktoe in 2010 and 1,119 Ktoe in 2020.

Monthly solar energy potential of Turkey is given in Table 1. Solar energy potential according to the geographical regions is given in Table 2.

However it has been recognized that the existing meteorological data is lower than the actual solar energy data of Turkey. EIE and DMI have been taking new measurements since 1992 to determine the more accurate solar energy data. Although the measurements have not been completed yet, the collected data indicates that the actual solar energy radiation values are 20-25% higher than the existing data.

A model was developed with the data from the 8 measurement stations of EIE and with the data from the DMI measurement stations. Accordingly, the solar radiation and insolation values are calculated for 57 cities of Turkey. The study is published as a report.

| TABLE 1 MONTHLY AVERAGE SOLAR POTENTIAL OF TURKEY |
| --- |
| MONTHS | MONTHLY TOTAL SOLAR ENERGY (Kcal/cm2-month) (kWh/m2-month) | SUNSHINE DURATION (hours /month) |
| January | 4.45 | 51.75 | 103.0 |
| February | 5.44 | 63.27 | 115.0 |
| March | 8.31 | 96.65 | 165.0 |
| April | 10.51 | 122.23 | 197.0 |
| May | 13.23 | 153.86 | 273.0 |
| June | 14.51 | 168.75 | 325.0 |
| July | 15.08 | 175.38 | 365.0 |
| August | 13.62 | 158.40 | 343.0 |
| September | 10.60 | 123.28 | 280.0 |
| October | 7.73 | 89.90 | 214.0 |
| November | 5.23 | 60.82 | 157.0 |
| December | 4.03 | 46.87 | 103.0 |
| TOTAL | 112.74 | 1311 | 2640 |
| AVERAGE | 308.0 cal/cm2-day | 3.6 kWh/m2-day | 7.2 hours/day |

Source: DMI, EIE

| TABLE 2 REGIONAL DISTRIBUTION OF SOLAR ENERGY POTENTIAL OF TURKEY |
| --- |
| REGION | TOTAL SOLAR RADIATION (kWh/m2-year) | SUNSHINE DURATION (hours/year) |
| Southeastern Anatolia | 1460 | 2993 |
| Mediterranean | 1390 | 2956 |
| East Anatolia | 1365 | 2664 |
| Central Anatolia | 1314 | 2628 |
| Aegean | 1304 | 2738 |
| Marmara | 1168 | 2409 |
| Black Sea | 1120 | 1971 |

Source: DMI, EIE

Total Solar Radiation (KWh/m2 – year)

Source: EIE

Irradiation & Solar ELECTRICITY Potential

| Turkey | Global yearly irradiation (kWh/m2) | Solar electricity generated from 1kWp (kWh/kWp)* |
| --- | --- | --- |
|  | min | min_urb5 | countr_avg | max_urb95 | max | min | min_urb5 | countr_avg | max_urb95 | max |
| Horizontal mounting | 1119 | 1313 | 1541 | 1683 | 1833 | 839 | 985 | 1156 | 1263 | 1375 |
| Optimum angle mounting | 1172 | 1454 | 1724 | 1894 | 2051 | 879 | 1090 | 1293 | 1421 | 1538 |
| Vertical mounting | 626 | 920 | 1089 | 1186 | 1282 | 470 | 690 | 817 | 890 | 962 |
| * performance ratio of the PV system = 0.75 |  |  |  |  |  |  |

| All year optimum angle (degrees) |
| --- |
|  | min | min_urb5 | countr_avg | max_urb95 | max |
| Turkey | 14 | 30 | 32 | 32 | 33 |

| Difference between "optimum angle" and "horizontal" mounting |
| --- |
|  | Difference in yearly irradiation (kWh/m2): OPT-HORIZ | Solar electricity generated from 1kWp (kWh/kWp)* | Difference in yearly irradiation (%): (OPT-HORIZ)/HORIZ |
|  | min | min_ urb5 | countr_ avg | max_ urb95 | max | min | min_ urb5 | countr_ avg | max_ urb95 | max | min | min_ urb5 | countr_ avg | max_ urb95 | max |
| Turkey | 53 | 140 | 183 | 211 | 218 | 39 | 105 | 137 | 158 | 164 | 4,7 | 10,7 | 11,5 | 12,2 | 11,8 |
| Difference between "optimum angle" and "vertical" mounting |
|  | Difference in yearly irradiation (kWh/m2): OPT-VERT | Solar electricity generated from 1kWp (kWh/kWp)* | Difference in yearly irradiation (%): (VERT-OPT)/OPT |
|  | min | min_ urb5 | countr_ avg | max_ urb95 | max | min | min_ urb5 | countr_ avg | max_ urb95 | max | min | min_ urb5 | countr_ avg | max_ urb95 | max |
| Turkey | 546 | 533 | 635 | 708 | 769 | 409 | 400 | 476 | 531 | 576 | 46,3 | 35,6 | 34,9 | 36,0 | 36,7 |
| * performance ratio of the PV system = 0.75 |  |  |  |  |  |  |  |  |  |

| min |  | absolute country minimum (all data grid cells included) |
| --- | --- | --- |
| min_urb5 |  | 5% occurrence (only built-up residential areas) |
| countr_avg |  | country average (all data grid cells included) |
| max_urb95 |  | 95% occurrence (only built-up residential areas) |
| max |  | absolute country maximum (all data grid cells included) |

C. Domestic Production of Solar Panels

Solar Thermal Collectors

There are more than 50 companies in Turkey carrying out production of solar thermal collectors. The industry is well developed with high quality manufacturing and export capacity. Total production capacity is estimated to be 1 million m2, and total production volume is approximately 750 thousand m2. The exports volume is estimated to be 200 thousand m2 and the imports volume is negligible.

Photovoltaic Modules

The photovoltaic sector in Turkey is still fairly small, providing work for only a small number of employees. The main actors consist of several companies and a number of research institutes. There are approximately 30 companies which are operating in Turkey’s PV sector. The main business types are importer, wholesale supplier, system integrator and retail sales. The companies serve in the installation, engineering and project development sectors. PV modules, battery charge controllers and inverters are mainly imported. Batteries, solar lighting systems, etc., may be supplied by the domestic market. Some of the domestic products (batteries, tempered glass, etc.) are exported.

Three companies (Anel Group (www.anel.com.tr), Tera Solar (http://tera-solar.com) and DATATSP (http://datatsp.com)) in Turkey have recently started production of solar cells (photovoltaic modules). Still there is a significant potential for investment in this field.

| Producers of Solar Thermal Collectors in Turkey |
| --- |
| SERGÜN GÜNEŞ ENERJİSİ SİSTEMLERİ İML. SAN. LTD. ŞTİ. | Address: Hürriyet Mah. Atatürk Bulvarı No: 322 / Yeşilbayır - Antalya Phone: +90 (242) 444 07 01 Fax: +90 (242) 443 11 90 info@sergun.com www.sergun.com |
| HER-AY Güneş Enerjisi ve Termosifon İmalatı SaN. Ve Tic. Ltd. Şti. | Address:Bakırcılar Sanayi Horozluhan Mah. Adıbelli Sok. NO: 48 Selçuklu-Konya Phone: +90 (332) 248 48 58 Fax: +90 (332) 320 12 95 heray@heray.com.tr www.heray.com |
| DAĞSAN SOLAR ENERJİ SİSTEMLERİ | Address: 2. OSB Ulukavak Sok. No: 3 Konya Phone: +90 (332) 239 09 06 Fax : +90 (332) 239 09 08 |
| BURAK İNOKS SOLAR ISI SİSTEMLERİ SAN. VE TİC. A.Ş. | Address: Adana OSB Yakapınar/Adana Phone: +90 (322) 394 40 30 Fax: +90 (322) 394 40 33 |
| EZİNÇ METAL A.Ş. | Address: Organize Sanayi Bölgesi 23. Cad. No:31 38070 Kayseri Phone : +90 (352) 321 13 21(Pbx) Fax : +90 (352) 321 13 25 aezinc@ezincmetal.com www.ezinc.com.tr |
| ERASLANLAR GÜNEŞ ENERJİSİ SAN. TİC. LTD. ŞTİ. | Address: Cacabey 2. Çarşı Kemalhocaoğulları Apt. No:2 Merkez İlçe 40100 Kırşehir Phone: +90 (386) 212 15 00 Fax: +90 (386) 214 27 69 |
| DERYA GÜNEŞ KOLLEKTÖR A.Ş | Address: 3.Organize Sanayi Bölgesi Vali İhsandede Cad. 13.Sok. No:29 42050 Selçuklu Konya info@deryakollektor.com.tr Phone: +90 (332) 239 15 70 Fax: +90 (332) 239 15 62 |
| GÖKSAN A.Ş | dasci_27@mynet.com |
| AGES GUNES ENERJISI SAN. VE TIC. A.S. | Address: Millet Cad. Sim Apt. No: 2/A Meram Konya Phone: +90 (332) 320 12 00 Fax : +90 (332) 322 40 61 bilgi@ages.com.tr www.ages.com.tr |
| KOCSAN GÜNEŞ ENERJİSİ SAN. VE TIC. LTD.STI. | Address: Meram San. Sitesi Nilüfer Sok. No: 30 Meram Konya Phone: +90 (332) 320 51 86 Fax: +90 (332) 322 80 05 kocsan@kocsanenerji.com www.kocsanenerji.com |
| HÜRSAN GÜNEŞ ENERJİSİ LTD. ŞTİ. | Address : Anadolu Sanayi Sitesi Poyraz Koy Sok. No: 6 Selcuklu / Konya Phone : +90 (332) 249 30 77- 249 73 47-249 06 06 Fax : +90 (332) 251 88 10 hursansolar@hotmail.com |
| FENİŞ TEKNİK ÜRÜNLER A.Ş | Address: Beylikbağı Mah. İstanbul Cad. No:21 41400 Çayırova-Gebze/ Kocaeli Phone: +90 (262) 742 18 30 Fax: +90 (262) 742 18 37 fenisteknik@fenis.com.tr www.fentek.com.tr |
| EFSUN METAL ISI İMALAT İNŞ. TUR. TEK. SAN. VE TİC. LTD. ŞTİ. | Address: OSB Atatürk Bulvarı No: 4 Phone: +90 (242) 258 11 53 Fax: +90 (242) 258 10 72 info@efsunsolar.com www.efsunsolar.com |
| TANSUĞ MAKİNA SAN. VE TİC. KOLL. ŞTİ | Address: Adana-Ceyhan Yolu 10. Km 01340 İncirlik/Adana Phone: +90 (322) 346 49 00 Fax: +90 (322) 346 50 08 info@tansug.com.tr www.tansug.com.tr |
| TÜRKSAN GÜNEŞ ENERJİSİ | www.turksankollektor.com turksan@turksankollektor.com turksan42@mynet.com |
| ANT-SU GÜNEŞ ENERJİSİ | ibrahimgozutok@hotmail.com |
| KODSAN KAZAN A.Ş. | Address: OSB Karamanlılar Cad. No: 10 Sincan 06935 Ankara Phone: +90 (312) 267 07 67 Fax: +90 (312) 267 05 54 faruk@kodsan.com.tr info@kodsan.com.tr www.kodsan.com.tr |
| İZOCAM A.Ş | Address: İzocam A.Ş Dilovası Mevkii, 41455 Kocaeli Phone: +90 (262) 754 63 90 Fax : +90 (262) 754 66 88 izoposta@izocam.com.tr |

D. Domestic Market of Solar Panels

Main solar energy utilization in Turkey is the flat plate collectors in the domestic hot water systems. Total area of installed collectors in Turkey is around 12 million m². The systems are mostly used in Aegean and Mediterranean regions. Total energy production equals to 420,000 TOE (ton oil equivalent).  The contribution of solar collectors to the primary energy production is given below:

| Year | Solar Energy Contribution (thousand TOE) |
| --- | --- |
| 1998 | 210 |
| 1999 | 236 |
| 2000 | 262 |
| 2001 | 290 |
| 2004 | 375 |
| 2007 | 420 |

Source: DMI, EIE

Utilization of photovoltaic systems is limited with the usage of some governmental organizations in remote service areas such as telecom stations, forest fire observation towers and highway emergency. Total installed peak power has reached about 3 MWp.

E. Foreign Trade

In Turkey, the volume of foreign trade of water heaters using solar energy and solar cells is in a trend of increase. Turkey is a net exporter of water heaters using solar power.

| Product | M/X | Unit | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | CAGR 07/02 %* | 2008/8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Water heaters using solar energy (HS code: 841919000012) | Import | 000 $ | 337 | 567 | 1,607 | 2,817 | 2,884 | 3,287 | 58 | 5,074 |
|  |  | tons | 82 | 181 | 453 | 977 | 992 | 1,130 | 69 | 1,536 |
|  | Export | 000 $ | 723 | 1,609 | 2,811 | 2,998 | 3,657 | 5,787 | 52 | 8,962 |
|  |  | tons | 306 | 498 | 755 | 812 | 956 | 1,341 | 34 | 1,720 |
| Solar cells (HS code: 854140900011) | Import | 000 $ | 388 | 247 | 835 | 1,189 | 233 | 2,128 | 41 | 3,276 |
|  |  | tons | 31 | 10 | 28 | 76 | 5 | 69 | 17 | 158 |

Source: Turkish Statistical Institute

*Compound annual growth rate between 2002&2007

Turkey imports water heaters using solar energy and solar cells mainly from China and Germany.

| Distribution of Imports of Water Heaters Using Solar Energy According to Countries, 2007 |
| --- |
| Country | Imports, 000 USD | Share % |
| China | 2,827 | 86 |
| Germany | 460 | 14 |
| Other | 0 | 0 |
| Total | 3,287 | 100 |

Source: Turkish Statistical Institute

| Distribution of Imports of Solar Cells According to Countries, 2007 |
| --- |
| Country | Imports, 000 USD | Share % |
| China | 786 | 37 |
| Germany | 721 | 34 |
| Japan | 486 | 23 |
| USA | 134 | 6 |
| Other | 0 | 0 |
| Total | 2,127 | 100 |

Source: Turkish Statistical Institute

Main destinations for Turkish exports of water heaters using solar energy are North Africa, Europe and Middle East.

| Distribution of Exports of Water Heaters Using Solar Energy According to Countries, 2007 |
| --- |
| Country | Exports, 000 USD | Share % |
| Marocco | 1,252 | 22 |
| Spain | 1,077 | 19 |
| Italy | 787 | 14 |
| Bulgaria | 545 | 9 |
| Portugal | 400 | 7 |
| Lebanon | 353 | 6 |
| Tunisia | 348 | 6 |
| France | 338 | 6 |
| Syria | 251 | 4 |
| T.R. Northern Cyprus | 192 | 3 |
| Other | 243 | 4 |
| Total | 5,787 | 100 |

Source: Turkish Statistical Institute

F. Research & Development in the Sector

Solar Energy Activities of Ege University - Solar Energy Institute

PV research has been realized in the Turkish university research laboratories to gain further experience in PV. The Solar Energy Institute, situated on the campus of Ege University in Izmir, was founded in 1978 for graduate education and research on Solar Energy and its applications. Ege University Solar Energy Institute is still the only research institute which mainly works on solar energy research topics. The institute also supports some projects of the municipalities and the other societies to increase the PV applications in Turkey. A project which is mainly financed by United Nations with the support of the institute has been executed as a solar lighting system in Gokceada which is the biggest island of Turkey. The studies are maintained in the production of organic dye-sensitized solar cells by the Solar Energy Institute of Ege University. Ege University Solar Energy Institute increases its PV power capacity by producing the solar modules with the lamination technique of silicon solar cells (Figure 2). The total PV capacity has reached to 24 kWp. The grid-connected PV power systems were followed/examined during the year (Figure 3). 14 kWp of the PV system has reorganized as a new stand-alone hybrid PV power system at the end of 2007 (Figure 4).

Source: IEA - PVPS Annual Report 2007 Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 Solar Energy Institute, Ege University

The recent historical development of the solar energy sector in Turkey can be summarized as follows:

2001

- The Solar Energy Institute of Ege University began to R&D studies on organic dye-sensitized solar cells to realize and to simplify the production processes and to lower the cost.

- A 14 kWp PV power plant was installed for starting up energy of some units in Berke Dam.

2002

- Installation of the largest grid connected PV power plant to date in Mugla University with 10,4 kWp capacity.

2004

- Mugla University increased the total PV power capacity to 54 kWp.

2005

- The Solar Energy Institute of Ege University installed 22,2 kWp PV grid-connected power plant in Izmir.

- TUBITAK (The Scientific and Technological Research Council of Turkey) initiated the first Formula-G solar car race between the Turkish universities. The TUBITAK plans to continue these solar car races in the next years in order to introduce solar electricity energy to the university students.

2006

- The Solar Energy Institute of Ege University set up a PV module production laboratory which is the first of its kind in a university.

- A Turkish company (Akkanat Technologies A.S.) began to produce PV modules with 5 MWp/year capacities in Istanbul (The manufacturer stopped the production at the present).

2007

- The first PV-wind-diesel generator hybrid power system was installed in a island by Girasolar Ltd. (Figure 5). Ege University Solar Energy Institute contributed to the project, as well. The project was performed on an island (Fethiye-Kizilada) which doesn’t have any utility grid connection. On the island, a restaurant provides the required energy with this hybrid system (17,5 kWp multi-crystalline solar modules, 15 kWp wind turbine, 35 kVA diesel generator, 48 V 3000 Ah battery capacity).

- In March 2007, the Energy Minister of Turkey opened a “Clean Energy House” in Pamukkale University, Denizli-Turkey. The house has a PV system that totals 5 kWp , which will also be used for hydrogen production.

- 30 kWp grid-connected PV power systems were installed in the TESCO-KIPA supermarkets in Marmaris and Kusadasi (totally 60 kWp PV systems) by Enisolar Ltd. (Figure 6). Some attractive small PV applications were also performed by Enisolar Ltd. in 2007 (Figure 7).

- TUBITAK-MRC has installed a stand alone renewable hydrogen demonstration park in Gebze. Ege University Solar Energy Institute was a participant of TUBITAK-MRC in the project. The autonomous system includes PV-wind-fuel cell hybrid power components (Figure 8).

- Turk Telecom has decided to install a 250 kWp photovoltaic power system for telecommunication systems. The company of Analtech Ltd. began to install these PV power systems in 2007. Some small PV systems were also installed for GSM telecommunication systems (Figure 9).

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Solar Energy Activities of EIE (General Directorate of Electrical Power Resources Survey and Development Administration)

Solar Energy Division of EIE has been carrying on research, development, information dissemination and demonstration activities since 1982.

1. THERMAL ACTIVITIES

##### Solar Collector Tests

Test platform was installed at the Renewable Energy Park of EIE, with the aim of supporting the manufacturers for a more efficient production.

Thermal performance experiments of the Turkish Standards on solar collectors “TS-3680” is also performed in the test laboratory.

Efficiency test of the collectors developed by any person, manufacturer or entity can also be performed in the test laboratory.

##### Ground Source Heat Pump

##### Ground source of heat pumps are a form of geothermal energy utilization. In order to investigate the technical and economic aspects of GSHP’s a demonstration system was installed in the Renewable energy Park of EİE in 2002.

##### Solar Cooker

##### Solar cookers concentrate the solar beam to reach to a high temperatures and are used especially in the under developed countries. The experimental solar cooker manufactured by EİE for demonstration purposes can reach to temperatures around 750 ºC.

##### 2. PHOTOVOLTAIC ACTIVITIES

##### Photovoltaic Lighting Units

Battery of the system is charged by the electricity generated by photovoltaic modules during the day. Currently 5 units are installed, 2 in Ankara AOÇ, 2 in Didim Research and Training Center of EIE and a 1 in the EIE building in Ankara. There is also a 160 Wp lighting system in Didim.

##### Photovoltaic Area Lighting

##### A 1000 Wp PV system is used for outdoor area lighting in Didim Research and Training Center.

##### Photovoltaic Water Pumping Systems

Of the systems that can be used in small scale agricultural irrigation, the first consists of 616 Wp PV modules, an inverter and a submersible pump. The economical calculations indicated that the system is economically competitive with diesel engines, in sites without grid.

Another water pumping system with 756 Wp power is installed at the Renewable energy Park of EIE.

##### Photovoltaic Traffic Warning System

##### The system consists of a 50 Wp pv module and 70 Ah battery, as well as a flashing lamp.

##### Grid-Connected 4,8 kWp Photovoltaic ystem

While the traditional utilization of photovoltaic system has been the remote areas without grid, in recent years, the number of grid connected PV systems has increased greatly.

Since Turkey has a very high electrification rate, a research on grid connected project was realized. As the first grid connected photovoltaic system in Turkey, the 4,8 kWp system installed in Didim Research and Training Center has been operating since 1998.

##### Grid-Connected 1,2 kWp Photovoltaic System

##### Another grid-connected system with a 1,2 kWp, was installed in EIE Renewable energy Park for demonstration purposes.

3. SOLAR ENERGY POTENTIAL ACTIVITIES

As a beginnig to the solar energy potential determination, EIE had evaluated the historical solar energy data measured by the State Meteorological Organization between the years of 1968-1982.The results were published in two reports in 1983. On the basis of these evaluations, it is concluded that the average annual value of sunshine hours is 2640 and annual average solar intensity is 3.6 kWh /m²-day, while maximum annual sunshine hours is 3016 hours and maximum solar intensity is 5,8 kWh/m2 –day.

Since the existing meteorological data was not technically sufficient, EIE has initiated a second project in cooperation with the State Meteorological Service. The aim of this project is to determine the actual solar potential nation wide with the help of data to be measured with 5 solar data acquisition systems. Data gathering period is 5 years for each station. The measured data are the total and diffuse solar radiation on the horizontal surface, bright sunshine duration and ambient temperature.

To this end, solar data acquisition systems have been installed in total 8 locations: Antalya, İzmir, Ankara, Aydın, Adana, Isparta, Kayseri and Balıkesir. The measurements in Antalya, İzmir and Aydın were completed.

| Antalya | İzmir | Aydın | Ankara |
| --- | --- | --- | --- |
| Adana | Isparta | Kayseri | Balıkesir |

With the data gathered from these measurements and by using the data from the stations of State Meteorological Organisation, the solar radiation and sunshine duration of 58 cities were calculated using a model. The report was published in 2001 as “The Solar Radiation and Sunshine Duration of Turkey”.

G. Governmental Institutions Operating in the Sector

EIE (General Directorate of Electrical Power Resources Survey and Development Administration), TUBITAK  (The Scientific and Technological Research Council of Turkey) - Marmara Research Center and some state universities (Ege University Institute of Solar Energy, Muğla University, METU, Kocaeli University, Fırat University, Harran University) are the institutions in Turkey operating in the field of solar energy research and development. Measurement of solar energy data is carried out by DMI (State Meteorological Services). EIE has been building up its own solar energy observation centres since 1991. Standards in the sector are determined by TSE (Turkish Standards Institution):

-TS 3680 – Solar Energy Collectors- Flat

-TS 3817 – Solar Energy – Water Heating Systems Manufacturing, Installation and Operation Rules

II. LegIslatIon & Government PolIcIes In THE Solar Energy Sector In Turkey

The energy policy objectives of Turkey essentially require diversifying the energy sources, to use domestic energy resources, to increase efficiency in electricity generation and consumption and to create an environment-friendly power system. It is clear that all of these objectives include increasing the share of renewable energy sources in total electricity generation. To this end, Turkish government passed the Law on Utilization of Renewable Energy Sources for the Purpose of Generating Electrical Energy (No. 5346) on May 10, 2005. According to this law;

- A legal person holding a generation license shall be awarded a “Renewable Energy Source Certificate” (YEK Certificate) by EMRA, for the purpose of identifying and monitoring the type of the source in purchasing and selling electric energy generated from renewable energy sources in domestic and international markets. The information relating to the amount of YEK certified electrical energy available for the implementations within the scope of this law shall be published by the Energy Market Regulatory Authority (“EMRA”) annually. Each of the legal entities holding a retail sale license shall purchase the amount of YEK certified electrical energy in accordance with the proportion of the energy amount they sold within the previous calendar year to the total electrical energy amount they sold in the country.

- The price to be applicable to the electrical energy to be purchased within the scope of this Law, for each year shall be the electricity average wholesale price in Turkey for the previous year as determined by EMRA. However, such applicable price may not be less than the Turkish Lira equivalent of 5 Euro Cent per kWh and may not exceed the Turkish Lira equivalent of 5.5 Euro Cent per kWh. However, legal entities that hold licenses based on renewable energy resources and which have the opportunity to sell above the limit of 5.5 Euro Cent kWh in the market shall benefit from this opportunity.

- Real persons and legal entities establishing an isolated or grid connected power plant with a maximum installed capacity of 1,000 kW for meeting solely their own needs, shall not pay service fees for these projects whose final project planning, master plan, prereviews or first studies have been prepared by DSI or EIE.

- Investments, within the framework of the provisions of this Law,in relation to;

a) Establishing energy generation facilities;

b) Provision of domestically manufactured electromechanical systems;

c) Research and development and manufacturing of electricity generation systems by utilizing solar cells and focusing units;

d) Research and development facilities for the generation of electric energy or fuel by utilizing biomass sources;

shall be eligible for incentives, based on a resolution determined by the Council of Ministers.

- As principal, housing units within the borders of administrative districts and municipalities located in regions where geothermal resources are sufficient to meet heating needs shall primarily be heated through geo and solar thermal sources.

- In case any real estate under the private ownership of the Forest Administration or Treasury, or under the discretion and disposal of the state is used for the purposes of generating electrical energy from renewable energy resources within the scope of this law, the Ministry of Environment and Forestry or the Ministry of Finance provides permission, leases, institutes an easement right or permits the use of the land for the plant, access roads and the energy transmission line up to grid connection point. With respect to power plants which shall be commissioned by the end of the year 2011, eighty five percent discount shall be applied to the fees regarding permit, lease, easement right and the right to use with respect to the plant, access roads and the energy transmission line up to the grid connection point during the first ten years of operation. With respect to forestlands, ORKÖY and Special Allowance for Tree Planting Revenues shall not be collected.

There is a draft law for renewable energy expected to be passed by the parliament in 2010. In accordance with this law, it is expected that the tariffs will become higher for the purchase of electric energy generated by renewable energy resources and domestic production of renewable energy systems will be supported.

Moreover, according to the Electricity Market Law (No. 4628), renewable energy systems with an installed capacity under 500 kw are not required to establish themselves as companies and obtain a license and are allowed to sell excess power to the grid.

Electricity Market Licensing Regulation has also some provisions supporting renewable energy investments:

- The legal entities applying for licenses for construction of facilities based on domestic natural resources and renewable energy resources shall only pay one percent of the total licensing fee. The generation facilities based on renewable and domestic energy resources shall not pay annual license fees for the first eight years following the facility completion date inserted in their respective licenses.

- The legal entities engaged in generation activity at facilities based on renewable energy resources may purchase electricity from private sector wholesale companies on the condition not to exceed the annual average generation amounts indicated in their licenses in a calendar year.

- Applicable for sales to non eligible consumers; if the price of electricity generated at generation facilities based on renewable energy resources is equal to or lower than the sales price of TETAŞ and if there is no cheaper alternative, the retail licensees shall be obliged purchase such energy for the purposes of re-sale to the non-eligible consumers.

- The autoproducer and autoproducer group licensees engaged in generation activity at facilities based on renewable energy resources may purchase electricity from private sector wholesale companies on the condition not to exceed the annual average generation amounts indicated in their licenses in a calendar year.

- TEIAS and/or distribution licensees shall assign priority for system connection of generation facilities based on domestic natural resources and renewable resources.

The procedures and principles of granting YEK Certificates are determined by the “Regulation on the Principles and Procedures for Granting Renewable Energy Resources” issued on Oct. 4, 2005.

In addition, an invesment in the renewable energy sector may benefit from general investment incentive program and incentives for priority development regions, as well as from incentives for R&D investments within the scope of the Law Concerning Support of Activities of Researches and Development bearing date Feb. 28, 2008, and number 5746.

There is no legal obstacle for further investments in wind and solar energy projects in Turkey; however, the major bottleneck existing for further wind energy generation projects are the lack of sufficient infrastructure (e.g. missing transmission lines) and high cost of transmission lines. There is no application date set for coming wind generation licenses in Turkey. The future licenses for energy generation is dependent on TEIAS (Turkish Electricity Transmission Company).

# Footnotes

Source: European Solar Thermal Industry Federation, Sun in Action II – A Solar Thermal Strategy for Europe, Volume 2, The Solar Thermal Sector Country by Country - 21 National Reports, April 2003.

Source: EIE

PVGIS © European Communities, 2001-2008

Source: Šúri M., Huld T.A., Dunlop E.D. Ossenbrink H.A., 2007. Potential of solar electricity generation in the European Union member states and candidate countries. Solar Energy, 81, 1295–1305. http://dx.doi.org/10.1016/j.solener.2006.12.007

Source: EIE

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University.

These companies are the members of the International Solar Energy Society – Turkish Section, www.gunder.org.tr

Source: EIE

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Source: IEA - PVPS Annual Report 2007 - Solar Energy Institute, Ege University

Source: www.eie.gov.tr

# Text boxes

Solar Energy in Turkey